## Slide 1: Dynamic Fault-Tolerance and Task Scheduling in Distributed Systems
Masters Thesis by Philip ståhl and jonatan broberg

## Slide 2: Agenda
Introduction and goal
Related work
System model
Reliability model
Self-adapting model
Calvin
Implementation
Experiments
Future Work

## Slide 3: Introduction
Reliability of applications of services in running in distributed environments
Problems:
  More resources --> higher probability that one will fail

## Slide 4: Goal
Devise a method for dynamically ensuring a certain reliability level applications or services running in distributed environments.
Design a reliability model for expressing the reliability for an application running in a distributed environment
Design a framework which dynamically ensures a certain level of reliability by detecting node failures and adapting to changing system properties
  Reliability will be ensured by the use of replication
Implement and evaluate model using Calvin

## Slide 5: Related work
Most assume constant failure rates, as well as same failure rates for all nodes

## Slide 6: System model
We assume an interconnected set of computing resources (nodes), providing redundant paths and interconnectivity between all nodes.
All nodes are within the same cluster
  Latency is the same between all nodes

## Slide 7: Fault model / Limitations
We make the following assumptions:
  Fully reliable links, we only consider node failures
  Nodes are either operational or failed
  Node failures do not depend on the jobs running on them and the computations they perform
  Statistically independent failures

## Slide 8: Failure distribution
We assume failures follow a Poisson process
where is the failure rate, i.e. the average number of failures during a time t.
From a time t and a mean-time-between-failures (MTBF), can be calculated as
Resulting in

## Slide 9: Failure distribution
We are interested in knowing the probability of a node surviving a time t, i.e. no failures
The probability that a failure occurs is thereby

## Slide 10: Application
We limit ourselves by only considering stream processing applications.
A processing task S will receive input from a producer, transform it, and send the result to a consumer.
When replicating the task S, the replicas will not be synchronized. To avoid timing issues, it is assumed no external calls are made which depends on when the request is made.
The task S, performs deterministic calculations on the input. If the replicas all receive the same input, they will all produce the same result.

## Slide 11: Reliability definitions
Reliability of
  Meeting deadlines
  Producing the correct result
Our definition
Reliability of a task which is serving some kind of requests, is the probability that no data is lost. In a process with n task replicas, this corresponds to at least one replica is always running and serving requests.

## Slide 12: Reliability model
Reliability is “… at least one replica is up and running ...”
This corresponds to not all failing. For n nodes, this is

## Slide 13: Reliability model
Failures will happen
Failures must be detected and new replicas be created to fulfill the desired reliability
In order to create a new replica, at least one existing replica must be alive during the time it takes to replicate it
The reliability can therefore be expressed as “… at least one replica is up and running during a time t...”, where t is the time it takes from that a failure occurs until a new replica is operational
The time t consist of the time to detect failure, and the time it takes to create a new replica

## Slide 14: Reliability model cont’d
“… at least one replica is up and running during a time t...”

## Slide 15: Fault-tolerant model
Goal is to provide a certain level of reliability
Basic idea:
  Create enough replicas to reach the required reliability
  Detect failures and create new replicas if needed
  Optimize by choosing the most reliable nodes to place replicas on
  Update reliability for nodes as failures occur

## Slide 16: Ensuring reliability
Desired reliability:
Algorithm:

## Slide 17: Detecting node failure
Heartbeats are periodically sent between runtimes. If no heartbeat from a node is received within 500 ms, it is assumed dead.
  Frequency: 200 ms
  Timeout: 500 ms
Since we assume high bandwidth low latency connections, the time it takes to send the heartbeat is negligible.
This gives us a worst case scenario of detecting node failures of 500 ms, and best case of 300 ms.

## Slide 18: Detecting node failure - best and worst case
Worst: t = 500’ ms
Best: t = 300’ ms

## Slide 19: Handling node failure
When a node failure is detected, every node take the following steps:
Select a node among the remaining nodes, select the one with the highest ID
Send a lost node message to the selected node
Wait for reply
  If no reply is received - start over at 1
  If reply – we’re done
The node receiving the lost node messages will check whether or not new replicas are needed, and if so, send replication request to one of the nodes holding a replica. When done, it will send a reply to everyone it received a lost node message from.

## Slide 20: Handling node failure cont’d.

## Slide 21: Handling node failure cont’d.

## Slide 22: Handling node failure cont’d.

## Slide 23: Handling node failure cont’d.

## Slide 24: Handling node failure cont’d.

## Slide 25: Example – before failure

## Slide 26: Example – after failure

## Slide 27: Calvin
Calvin is an actor-based application environment for light-weight IoT applications. Its key components are
  runtimes
  actors
  applications
  and the use of Kademlia, a distributed hash table

## Slide 28: Calvin - runtime
A Calvin runtime is a self-managed container for application actors
Provides data transport between actors both within the same runtime and between different runtimes.

## Slide 29: Calvin - actor
An actor in Calvin consists of ports, actions, and preconditions under which actions can fire.
For each in-port there is a queue of messages, called tokens, to process. Each out-port has a queue of tokens to send to another actors in-port.
The state of an actor is used when migrating or replicating an actor and consists mainly of
  The type of actor
  Arguments needed to create the actor
  Port connections information
  Port queues

## Slide 30: Calvin - application
An application in Calvin is made up from a set of connected actors.
Example:
src : std.CountTimer(sleep=0.5)
id : std.Identity()
snk : io.Print()
src.integer > id.token
id.token > snk.token

## Slide 31: Changes made to Calvin
Replication
Fan-in/fan-out model – allowing multiple connections for an inport
Heartbeat system setup by each runtime creating a Heartbeat actor
  Listens for heartbeats
  Send heartbeats to other runtimes
Resource reporter – reports CPU usage to the other runtimes
Lost node handler – handles lost node
Replicator – replicates actors

## Slide 32: Experiments
We have conducted a set of various tests to prove the usefulness of our model.
The goal was to show our model
Dynamically ensures the required reliability is met, despite the event of node failures, by dynamically creating new replicas when old ones die
Uses the optimal number of replicas by choosing the most reliable nodes
Adapts to changing system properties
We also measured how the replication time varied depending on the state size, as the replication time is an important part of the reliability model.

## Slide 33: Experiments setup
A cluster of 6 servers were used in the experiments.
Server specification:
Intel(R) Xeon(R) CPU E5-2420 v2 of 2.20 GHz
24 GB RAM
Connected with a 1000 Mb/s link with a latency of less than 0.2 ms.
The average time t in the experiments were 520 ms.
  Of which 500 ms were the upper bound for detecting node failures

## Slide 34: Application used in experiments
The application used in the experiment consisted of three actors, a producer, service actor, and a consumer.

## Slide 35: Application used in experiments cont’d.

## Slide 36: Simulating node failures

## Slide 37: Ensuring a certain reliability
One Calvin runtime per server
MTBF for each runtime was 20 seconds
Required reliability: 0.98
Time t: 530 ms
Reliability of nodes: R(t) = e-t/MTBF = e-530/20000 = 0.97530
Number of replicas | Reliability
1 | 1 – (1 – R(t))1 = 0.97530
2 | 1 – (1 – R(t))2 = 0.99939
3 | 1 – (1 – R(t))3 = 0.99998

## Slide 38: Result

## Slide 39: Optimal number of replicas
Two Calvin runtimes per server
MTBFs varied
Required reliability: 0.999
Time t: 530 ms
Reliability of nodes:
MTBF | Reliability
7.5 | R(t) = e-t/MTBF = e-530/20000 = 0.93551
15 | R(t) = e-t/MTBF = e-530/20000 = 0.96722
40 | R(t) = e-t/MTBF = e-530/20000 = 0.98758
Runtime | MTBF (s)
dave1 | 7.5
dave2 | 7.5
tim1 | 7.5
tim2 | 7.5
kevin1 | 15
kevin2 | 15
mark1 | 15
mark2 | 40
jerry1 | 40
jerry2 | 40

## Slide 40: Optimal number of replicas cont’d.
Reliability:
Number of replicas | Nodes | Reliability
2 | 2 * MTBF(7.5) | 1 – (1 – R7.5(t))2 = 0.99534
3 | 3 * MTBF(7.5) | 1 – (1 – R7.5(t))3 = 0.99968
2 | 2 * MTBF(15) | 1 – (1 – R15(t))2 = 0.99879
3 | 3 * MTBF(15) | 1 – (1 – R15(t))3 = 0.99996
1 | 1 * MTBF(40) | 1 – (1 – R40(t)) = 0.98683
2 | 2 * MTBF(40) | 1 – (1 – R40(t))2 = 0.99983
3 | 1 * MTBF(15) + 2 * MTBF(7.5) | 1 – (1 – R15(t)) * (1 – R7.5(t)) 2 = 0.99984
3 | 2 * MTBF(15) + 1 * MTBF(7.5) | 1 – (1 – R15(t))2 * (1 – R7.5(t)) = 0.99991

## Slide 41: Result – total number of replicas

## Slide 42: Result – replicas per node (MTBF 7.5)

## Slide 43: Result – replicas per node (MTBF 15)

## Slide 44: Result – replicas per node (MTBF 40)

## Slide 45: Removing unnecessary replicas
One Calvin runtime per server
Three stable, Dave, Tim, Mark, while Kevin and Jerry were given a MTBF of 25 seconds
  Dave, Tim, and Mark, got default values of 10 seconds
Required reliability: 0.999
Time t: 530 ms
Reliability of nodes:
MTBF | Reliability
10 | R(t) = e-t/MTBF = e-530/20000 = 0.95123
25 | R(t) = e-t/MTBF = e-530/20000 = 0.98020

## Slide 46: Removing unnecessary replicas cont’d.
Reliability:
Number of replicas | Nodes | Reliability
1 | 1 * MTBF(10) | 1 – (1 – R10(t))1 = 0.95123
2 | 2 * MTBF(10) | 1 – (1 – R10(t))1 = 0.99762
3 | 3 * MTBF(10) | 1 – (1 – R10(t))1 = 0.99988
1 | 1 * MTBF(25) | 1 – (1 – R25(t))1 = 0.98020
2 | 2 * MTBF(25) | 1 – (1 – R25(t))2 = 0.99960
3 | 1 * MTBF(25) + 1 * MTBF(10) | 1 – (1 – R25(t)) * (1 – R10(t)) = 0.99892
3 | 1 * MTBF(25) + 2 * MTBF(10) | 1 – (1 – R25(t)) * (1 – R10(t))2 = 0.99994

## Slide 47: Result – total number of replicas

## Slide 48: Result – replicas per node (MTBF 10)

## Slide 49: Result – replicas per node (MTBF 25)

## Slide 50: Self-adapting
Two Calvin runtimes per server
Required reliability: 0.999
Time t: 530 ms
Killing nodes:

## Slide 51: Result – node reliabilities
MTBF is based on latest 3 values

## Slide 52: Result – number of replicas

## Slide 53: Replication time
Two runtimes, and one actor with one outgoing port.
The size of the actor state was measured, as well as the time to replicate the actor from one runtime to another.
The state was increased by increasing the size of the actors port queue.
Laptop specifications:
  Intel i5, 2.3 GHz
  4 GB 1333 MHz RAM
  SSD drive

## Slide 54: Result

## Slide 55: Result

## Slide 56: Future work
The reliability model is exchangeable. It can be extended through:
  Adding more parameter, e.g. considering link failures
  Applying machine learning
Adding a consensus algorithm
  Detect nodes producing the wrong result
The scheduling can be extended by
  Not placing replicas in the same physical location, e.g. in the same rack.
  Include nodes´ load and resources in the scheduling

## Slide 57: Considering load in the scheduling
We made an experiment where we had
  2 reliable nodes (MTBF = 40 s) and
  3 less reliable nodes (MTBF = 10 s).
First all nodes had a low load, then we increased the load on one of the more reliable nodes and later decreased it again.
We added a condition in the scheduling algorithm
  If load > MAX_PREFERRED_LOAD then place the task on another node if possible

## Slide 58: Considering load in the scheduling, cont’d.
[bild över usage]

## Slide 59: Considering load in the scheduling, cont’d.
[Bild över loaded nodes]

## Slide 60: Considering load in the scheduling, cont’d.
[Bild över unloaded nodes]